## Slide 1
IN THE NAME OF GOD
NMR Spectroscopy
Aref Honarparvaran
Master Student of Chemical Engineering
Supervisor: Dr Mehrnia
Advisor: Dr Pourasgharian Roudsari
Spring 1401

## Slide 2
Introduction
What is NMR and Why do we use it?
The difference between NMR and other analysis
  Mass spectroscopy (Example: C3H7Cl)
  FTIR (Many C….H vibrations)
  NMR (Is it ClCH2CH3 or H3CCHCH3 ???)
What is the principle of NMR?
Introduction
Principles
Sample preparation
Cl
Analysis

## Slide 3
Consider a hydrogen atom
Introduction
Principles
4
Acts like:
Other atoms can be act like magnet like C, F and P (CNMR, FNMR, PNMR)
  Odd number of protons
  Odd number of Neutrons
  Both (Deuterium)
Fig 1. Schematic of hydrogen atom and its similarity to magnet
Sample preparation
Analysis
B

## Slide 4
Principles
Introduction
5
magnet
NMR
magnet
NMR
B
Applied magnetic field
I) Deshielded
Fig 2. Magnet spinning inside magnetic field (Deshielded)
Sample preparation
Analysis

## Slide 5
Introduction
Principles
6
magnet
NMR
Diamagnetic shielded
Diamagnetic shield disturbs the magnet from rotating
II) Shielded
Fig 3. Magnet spinning inside magnetic field (Shielded)
Applied magnetic field
Local magnetic field
Effective magnetic field
Sample preparation
Analysis
B
Applied magnetic field

## Slide 6
6
B effective= B Applied – B local
I) B effective = B Applied – 0
II) B effective = B Applied – ( )
Principles
Introduction
Sample preparation
Analysis
Deshielded
Shielded

## Slide 7
Introduction
Principles
7
magnet
NMR
magnet
NMR
rf radiation
rf radiation
E1
E2
magnet
NMR
magnet
NMR
E1
E2
α-spin state
β-spin state
β-spin state
>
Fig 5. Applying rf radiation for atom resonance
Sample preparation
Analysis

## Slide 8
9
E1
E2
Energy
Downfield Signal
Upfield Signal
0
(Shielded)
(Deshielded)
Fig 6. Energy required for shielded and deshielded atoms to resonate
Principles
Introduction
Sample preparation
Analysis

## Slide 9
8
Shielded
B effective
E
Downfield
Deshielded
B effective
E
Upfield
Principles
Introduction
Sample preparation
Analysis

## Slide 10
10
ClCH2CH3
Example:ClCH2CH3
Cl atom can pull the electrons adjacent to hydrogen towards itself due to its high electronegativity and H becomes deshielded.
This is what exactly happens to another H atom but it is less severe, So it becomes more shielded.
ClCH2CH3
Deshielded
Shielded
Sample preparation
Principles
Introduction
Analysis

## Slide 11
Sample preparation
Introduction
Principles
11
Useful Solvents for NMR
CDCl3
DMSO-d6
D2O
Acetone-d6
Analysis

## Slide 12
Introduction
Principles
13
HNMR, PNMR, FNMR
CNMR
5-10 mg sample in 0.5-0.7 solvent
30-40 mg sample in 0.5-0.7 solvent
Samples must be dried as possible before dissolving in solvent (freeze drying method is helpful)
Sample preparation
Analysis

## Slide 13
12
TMS (Tetramethylsilane) has been chosen as the reference material because its 12 protons are absorbed at equal frequency.
δ:
δ is defined to solve the problem of showing incomparable absorbing frequencies when using different magnets.
δ = *
Result & Discussion
Introduction
Materials &
Method
Conclusion
Analysis

## Slide 14
14
Result & Discussion
Introduction
Materials &
Method
Conclusion
Analysis
Analysis of HNMR